# A Novel Integrated Stability Control Based on Differential Braking and Active Steering for Four-axle Trucks

### 论文摘要

Di erential braking and active steering have already been integrated to overcome their shortcomings. However, existing research mainly focuses on two-axle vehicles and controllers are mostly designed to use one control method to improve the other. Moreover, many experiments are needed to improve the robustness; therefore, these control methods are underutilized. This paper proposes an integrated control system specially designed for multi-axle vehicles, in which the desired lateral force and yaw moment of vehicles are determined by the sliding mode control algorithm. The output of the sliding mode control is distributed to the suitable wheels based on the abilities and potentials of the two control methods. Moreover, in this method, fewer experiments are needed, and the robustness and simultaneity are both guaranteed. To simplify the optimization system and to improve the computation speed, seven simple optimization subsystems are designed for the determination of control outputs on each wheel. The simulation results show that the proposed controller obviously enhances the stability of multi-axle trucks. The system improves 68% of the safe velocity, and its performance is much better than both di erential braking and active steering. This research proposes an integrated control system that can simultaneously invoke di erential braking and active steering of multi-axle vehicles to fully utilize the abilities and potentials of the two control methods.

### 论文目录

### 文章来源

类型: 期刊论文

作者: Buyang Zhang,Changfu Zong,Guoying Chen,Yanjun Huang,Ting Xu

来源: Chinese Journal of Mechanical Engineering 2019年01期

年度: 2019

分类: 工程科技Ⅱ辑

专业: 汽车工业

单位: College of Automotive Engineering, Jilin University,State Key Laboratory of Automotive Simulation and Control, Jilin University,College of Mechanical and Mechatronics Engineering, University of Waterloo

基金: Supported by National Natural Science Foundation of China(Grant No.51505178),China Postdoctoral Science Foundation(Grant No.2014M561289)

分类号: U463.6

页码: 174-194

总页数: 21

文件大小: 4297K

下载量: 51

### 相关论文文献

- [1].The Indirect Shared Steering Control Under Double Loop Structure of Driver and Automation[J]. IEEE/CAA Journal of Automatica Sinica 2020(05)

- [2].Research on Energy Saving Technology of Load Sensitive Variable Steering System for Vehicles[J]. International Journal of Plant Engineering and Management 2020(01)

- [3].Wald tests for signal detection when uncertainty exists in a target's spatial-temporal steering vector[J]. Science China(Information Sciences) 2020(08)

- [4].Driver-automation shared steering control for highly automated vehicles[J]. Science China(Information Sciences) 2020(09)

- [5].Simulation of beam steering control in arrayed liquid prisms system based on electrowetting-on-dielectric[J]. Optoelectronics Letters 2020(05)

- [6].Active steering control strategy for articulated vehicles[J]. Frontiers of Information Technology & Electronic Engineering 2016(06)

- [7].Theoretical and Experimental Investigation of Driver Noncooperative-Game Steering Control Behavior[J]. IEEE/CAA Journal of Automatica Sinica 2021(01)

- [8].Characterizing Bell nonlocality and EPR steering[J]. Science China(Physics,Mechanics & Astronomy) 2019(03)

- [9].Polarization-independent two-dimensional beam steering using liquid crystal optical phased arrays[J]. Chinese Optics Letters 2017(10)

- [10].Performance optimization of electric power steering based on multi-objective genetic algorithm[J]. Journal of Central South University 2013(01)

- [11].Integration optimization of novel electric power steering system based on quality engineering theory[J]. Journal of Central South University 2013(06)

- [12].H_∞ control of novel active steering integrated with electric power steering function[J]. Journal of Central South University 2013(08)

- [13].Multi-objective optimization of active steering system with force and displacement coupled control[J]. Journal of Central South University 2012(04)

- [14].Electrical power assisted steering for EVs and HEVs[J]. Engineering Sciences 2011(01)

- [15].Primary studies on integration optimization of differential steering of electric vehicle with motorized wheels based on quality engineering[J]. Science China(Technological Sciences) 2011(11)

- [16].Beam steering approach for high-precision spatial light modulators[J]. Chinese Optics Letters 2010(11)

- [17].Model development and parameter investigation of a column-type electric power steering system[J]. Journal of Shanghai University(English Edition) 2009(06)

- [18].Robust control for active suspension system under steering condition[J]. Science China(Technological Sciences) 2017(02)

- [19].Path planning and stability control of collision avoidance system based on active front steering[J]. Science China(Technological Sciences) 2017(08)

- [20].Mixture steering law design for control moment gyroscopes[J]. Science China(Physics,Mechanics & Astronomy) 2014(01)

- [21].Analysis of steering performance of differential coupling wheelset[J]. Journal of Modern Transportation 2014(02)

- [22].Multidiscipline collaborative optimization of differential steering system of electric vehicle with motorized wheels[J]. Science China(Technological Sciences) 2012(12)

- [23].Control strategy of a novel electric power steering system integrated with active front steering function[J]. Science China(Technological Sciences) 2011(06)

- [24].On fractional control method for four-wheel-steering vehicle[J]. 中国科学:技术科学 2010(03)

- [25].High-transmittivity non-periodic sub-wavelength high-contrast grating with large-angle beam-steering ability[J]. Chinese Optics Letters 2014(12)

- [26].Dynamics of electromagnetic slip coupling for hydraulic power steering application and its energy-saving characteristics[J]. Journal of Central South University 2015(05)

- [27].A Novel Estimating Method for Steering Efficiency of the Driver with Electromyography Signals[J]. Chinese Journal of Mechanical Engineering 2014(03)

- [28].Function of shoulder muscles of driver in vehicle steering maneuver[J]. Science China(Technological Sciences) 2012(12)

- [29].On fractional control method for four-wheel-steering vehicle[J]. Science in China(Series E:Technological Sciences) 2009(03)

- [30].An improved constrained steering law for SGCMGs with DPC[J]. Acta Mechanica Sinica 2009(05)

本文来源: https://www.lunwen66.cn/article/a1160c7be435244fd39e437c.html